## Slide 1
Microprocessor on FPGA
Presented By: Elie Youssef
Instructor: Bilal Moussa
Microprocessor & ES
Fall 2022-2023
CPU

## Slide 2
Introduction
Embedded microprocessor has been used as a tool for technological innovations and cost reduction
For a design to be competitive, its processor must be inexpensive, flexible, adaptable, fast and reconfigurable.
All these characteristics can be found using a Field-Programmable gate arrays as a design tool
GOAL OF THIS PROJECT: Realize an 8-bit FPGA based simple processor

## Slide 3
8-bit Processor Specs
MUXA
MUXB
Start
16-word memory with 8-bit words
Four 4-bit registers

## Slide 4
Instruction Type
Op | Op | CC | CC | SRC | SRC | DST | DST
7 6 5 4 3 2 1 0
1 | 1 | CC | CC | Address
7 6 5 4 3 2 1 0
1 | 1 | 0 | 0 | H | L | DST | DST
7 6 5 4 3 2 1 0
1) Register Instructions
2) Branch Instructions
CC=01
or
CC=10 and Ci=1
or
CC=11 and Ci=0
3) Halt/IO Instructions
L=1 => enable loading from a fixed register to the data register specified
H=1 => display the information located in the destination register on the seven-segment display
L=1 and H=1 => Nothing happens

## Slide 5
Control Unit
MUXA
MUXB
Start

## Slide 6
Control Unit
CLK
Control_unit
Reset
start
src
op
cc
c
st
Fetch_en
Incr_pc
Src_reg_en
Ci_out_en
addsub
din
ssd
Pc_reg
ALUout
MUXA_out
Ci_out
dst_reg_en
Enable fetch of inst from memory to IR
Show State type
Enable incrementation of pc
Enable to send value from source register along carry to ALU
Enable for address bits in IR to go to pc
Enable ci_out input to muxb
0 for add and 1 for sub
Enable inputs bits to be loaded into register pointed by dst
Enable for display content of dst register on 7seg
Enable to send value from destination register
Enable for output of alu to go to dest reg
Enable for outp of alu in first clock cycle to go a second time to alu
Carry out

## Slide 7
Control Unit
Finite State Machine

## Slide 8
begin
P1:process (clk)
variable L: std_logic;
variable H: std_logic;
variable ci: std_logic;
variable cycle_count: natural;
begin
if reset='1' then
state<=initial;
elsif rising_edge (clk) then
case state is
when initial=>
if start='1' then
state<=zero;
incr_pc<='0';
end if;
if cycle_count<1 then
cycle_count:=cycle_count+1;
else
state<=one;
cycle_count:=0;
fetch_en<=‘0';
end if;;
when zero=> fetch_en<='1';
incr_pc<='0';
src_reg_en<='0';
dst_reg_en<='0';
ci_out_en<='0';
addsub<='0';
din<='0';
ssd<='0’;
pc_reg<='0';
ALUout<='0';
MUXA_out<='0';
ci_out<='0’;
L:='0';
H:='0';
ci:='0';
--Fetch

## Slide 9
elsif (H='1') then;
incr_pc<='1';
dst_reg_en<='1';
ssd<='1';
state<=initial;
end if;
elsif op="11" and (cc="01" or ((cc="10") and (ci='1')) or ((cc="11") and (ci='0'))) then
pc_reg<='1';
state<=zero;
fetch_en<='1';
end if;
when one=>
if (op="00" or op="01" or op="10") then
state<=two;
src_reg_en<='1'; ci_out_en<='1'; addsub<='0’; -- Src+carry
if cc="00" then ci:='0'; elsif cc="01" then ci:='1';
elsif cc="10" then ci:=C; else ci:=not C; end if; ci_out<=ci;
elsif op="11" and cc="00" then L:=src(0);
H:=src(1);
if (L='1') then
if cycle_count<1 then cycle_count:=cycle_count+1;
else cycle_count:=0; incr_pc<='1';
din<='1'; state<=zero; end if;
Op | Op | CC | CC | SRC | SRC | DST | DST
1 | 1 | CC | CC | Address
1 | 1 | 0 | 0 | H | L | DST | DST
--Decode

## Slide 10
when two=>
src_reg_en<='0';
incr_pc<='1’;
if op="00" then
state<=three; elsif op="01" then
MUXA_out<='1';
dst_reg_en<='1';
ci_out_en<='0';
addsub<='0';
state<=three;
incr_pc<='0';
dst_reg_en<='0';
ALUout<='1';
when four=>
ALUout<='0’;
fetch_en<='1';
state<=initial;
end case;
end if;
end process P1;
st<=state;
elsif op="10" then
MUXA_out<='1';
dst_reg_en<='1';
ci_out_en<='0';
addsub<='1'; state<=three; end if;
end if;
when three=>
state<=four;
MUXA_out<='0';
--Execute arithmetic

## Slide 11
Switch Register
MUXA
MUXB
Start

## Slide 12
D
Op | Op | CC | CC | SRC | SRC | DST | DST
1)
7 6 5 4 3 2 1 0
1 | 1 | CC | CC | Address
7 6 5 4 3 2 1 0
1 | 1 | 0 | 0 | H | L | DST | DST
7 6 5 4 3 2 1 0
2)
3)
Sync_Reset
7 6 5 4 3 2 1 0
Q
entity switch_reg is
port(
Q : out std_logic_vector(7 downto 0);
Clk : in std_logic;
sync_reset: in std_logic;
D : in std_logic_vector(7 downto 0)
);
end switch_reg;
process(Clk)
begin
if(rising_edge(Clk)) then
if(sync_reset='1') then
Q <= (others => '0');
else
Q <= D;
end if;
end if;
end process;
CLK
switch_reg
Goes to memory

## Slide 13
Memory
MUXA
MUXB
Start

## Slide 14
Inst_addr
7 6 5 4 3 2 1 0
addr
Sel_l
Wr_l
entity memory is port(
inst_addr: in std_logic_vector(7 downto 0);
sel_l: in std_logic;
wr_l: in std_logic;
inst_mem: out mem_array_type:=(
"00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000");
q: out std_logic_vector(7 downto 0) :="00000000";
addr: in natural
);
end memory;
Inst_mem
.
.
.
0)
15)
outp
And_gate
q
package mem_array is
type mem_array_type is array(0 to 15) of std_logic_vector(7 downto 0);
end package;
architecture behav of memory is
signal outp:std_logic;
signal and_gate:std_logic;
signal inst : mem_array_type:=(
"00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000");
Begin
outp<=not sel_l;
and_gate<=(not sel_l) and (not wr_l);
inst(addr)<=inst_addr when and_gate='1';
q<=inst(addr) when outp='1' and and_gate='0';
inst_mem<=inst;
end behav;
memory
q

## Slide 16
Inst_addr
7 6 5 4 3 2 1 0
addr
Sel_l
Wr_l
entity memory is port(
inst_addr: in std_logic_vector(7 downto 0);
sel_l: in std_logic;
wr_l: in std_logic;
inst_mem: out mem_array_type:=(
"00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000");
q: out std_logic_vector(7 downto 0) :="00000000";
addr: in natural
);
end memory;
Inst_mem
.
.
.
0)
15)
outp
And_gate
q
package mem_array is
type mem_array_type is array(0 to 15) of std_logic_vector(7 downto 0);
end package;
architecture behav of memory is
signal outp:std_logic;
signal and_gate:std_logic;
signal inst : mem_array_type:=(
"00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000","00000000");
Begin
outp<=not sel_l;
and_gate<=(not sel_l) and (not wr_l);
inst(addr)<=inst_addr when and_gate='1';
q<=inst(addr) when outp='1' and and_gate='0';
inst_mem<=inst;
end behav;
memory
q

## Slide 17
Multiplexer-D
MUXA
MUXB
Start

## Slide 18
entity muxd is port (
start,incr_pc:in std_logic;
enable:out std_logic);
end muxd;
architecture m of muxd is
begin
enable<='1' when (start='1' and incr_pc='1') else '0';
end m;
start
Incr_pc
enable
muxd
Input User
Control_Unit
Incr_pc: Enable incrementation of pc

## Slide 19
Program Counter
MUXA
MUXB
Start

## Slide 20
Incr_pc
reset
counter
CLK
PC
Pc_reg
src
dst
Control Unit
Pc_reg: In case of Branch operation where we need to load data into specific address, enable for address bits in IR to go to pc
entity pc1 is port (
clk,reset,incr_pc,pc_reg:in std_logic;
src,dst:in std_logic_vector(1 downto 0);
counter:out integer natural);
end pc1;
architecture count of pc1 is
signal cnt:natural;
begin
P1:process (clk,reset)
begin
if reset='1' then
cnt<=0;
elsif rising_edge (clk) then
if pc_reg='1' then
cnt<=to_integer(unsigned(src & dst));
elsif incr_pc ='1' then
cnt<=cnt+1;
end if;
end if;
end process P1;
counter<=cnt;
end count;
Goes to addr of memory

## Slide 21
Branch Instruction go to memory’s 2nd address
1 | 1 | CC | CC | Address
7 6 5 4 3 2 1 0

## Slide 22
Inst_addr
7 6 5 4 3 2 1 0
addr
Sel_l
Wr_l
entity memory is port(
inst_addr:in std_logic_vector(7 downto 0);
sel_l:in std_logic;
wr_l:in std_logic;
inst_mem:out mem_array_type;
q:out std_logic_vector(7 downto 0);
addr:in integer range 0 to 7 -- to be replaced by counter
);
end memory;
Inst_mem
.
.
.
0)
7)
outp
And_gate
q
package mem_array is
type mem_array_type is array(0 to 7) of std_logic_vector(7 downto 0);
end package;
architecture behav of memory is
signal outp:std_logic;
signal and_gate:std_logic;
signal inst : mem_array_type;
begin
outp<=not sel_l;
and_gate<=(not sel_l) and (not wr_l);
inst(addr)<=inst_addr when and_gate='1';
q<=inst(addr) when outp='1' and and_gate='0';
inst_mem<=inst;
end behav;
memory
q

## Slide 23
Instruction Register
MUXA
MUXB
Start

## Slide 24
en
CLK
Instruction_register
inst
op
cc
src
dst
Op | Op | CC | CC | SRC | SRC | DST | DST
7 6 5 4 3 2 1 0
entity instruction_register is port (
clk:in std_logic;
en:in std_logic;
inst:in std_logic_vector (7 downto 0);
op,cc,src,dst:out std_logic_vector(1 downto 0));
end instruction_register;
architecture ir of instruction_register is
begin
P1:process (clk)
begin
if rising_edge (clk) then
if en='1' then
op<=inst(7 downto 6);
cc<=inst(5 downto 4);
src<=inst(3 downto 2);
dst<=inst(1 downto 0);
end if;
end if;
end process P1;
end ir;
Control_Unit
Fetch_enable: Enable fetch of inst from memory to IR

## Slide 25
Demultiplexer
MUXA
MUXB
Start

## Slide 26
din
dst
dmux
en1
en2
en3
en4
entity dmux is port (
dst: in std_logic_vector (1 downto 0); --sel
din,alu_out: in std_logic;
en1,en2,en3,en4: out std_logic);
end dmux;
architecture d of dmux is
begin
en1<='1' when ((alu_out='1' or din='1') and dst="00") else '0';
en2<='1' when ((alu_out='1' or din='1') and dst="01") else '0';
en3<='1' when ((alu_out='1' or din='1') and dst="10") else '0';
en4<='1' when ((alu_out='1' or din='1') and dst="11") else '0';
end d;
Alu_out
Din: enable for inputs bits loaded into register pointed by dst
Alu_out: enable for output of alu to go to dest reg
Enable to send value in source register along carry to ALU

## Slide 27
Four 4-bit registers
MUXA
MUXB
Start

## Slide 28
reset
CLK
reg
en1
q1
3 2 1 0
en2
en3
en4
q2
q3
q4
d1
d2
d3
d4
entity reg is port (
clk,reset:in std_logic;
en1,en2,en3,en4:in std_logic;
q1,q2,q3,q4:out std_logic_vector(3 downto 0) :="0000";
d1,d2,d3,d4:in std_logic_vector (3 downto 0));
end reg;
architecture r of reg is
begin
reg1: entity RisingEdge_DFlipFlop_SyncReset port map (q1,clk,en1,reset,d1);
.
.
.
reg4: entity RisingEdge_DFlipFlop_SyncReset port map (q4,clk,en4,reset,d4);
end r;
if(rising_edge(Clk)) then
if(sync_reset='1') then
Q <= (others => '0');
elsif(en = '1') then
Q <= D;
end if;
end if;
Data

## Slide 29
1 | 1 | 0 | 0 | H | L | DST | DST
7 6 5 4 3 2 1 0
L=1=> Load value from Switch register in register reg2

## Slide 31
1 | 1 | 0 | 0 | H | L | DST | DST
7 6 5 4 3 2 1 0
L=1=> Load value from Switch register in register reg1

## Slide 33
Multiplexer 1
MUXA
MUXB
Start

## Slide 34
Val_in1
Sel (src)
mux1
Value coming from either reg1,2,3 or 4
Val_in2
Val_in3
Val_in4
Val_out
entity mux1 is port (
sel:in std_logic_vector (1 downto 0);
en:in std_logic;
val_in1,val_in2,val_in3,val_in4: in std_logic_vector (3 downto 0);
val_out: out std_logic_vector (3 downto 0) :="0000");
end mux1;
architecture m1 of mux1 is
begin
val_out<=val_in1 when (sel="00" and en='1') else val_in2 when (sel="01" and en='1')
else val_in3 when (sel="10" and en='1') else val_in4
when (sel="11" and en='1') else "0000";
end m1;
en
Src_reg_en:Enable to send value from source register along carry to ALU

## Slide 35
Multiplexer A
MUXA
MUXB
Start

## Slide 36
Alu_out
en
muxa
Val_out
entity muxa is port (
alu_out,d_reg:in std_logic_vector (3 downto 0);
en:in std_logic;
val_out:out std_logic_vector (3 downto 0) :="0000");
end muxa;
architecture ma of muxa is
begin
val_out<=alu_out when en='1' else d_reg;
end ma;
D_reg
Muxa_out : Enable for outp of alu in first clock cycle to go a second time to alu
Value from ALU

## Slide 37
Multiplexer 2
MUXA
MUXB
Start

## Slide 38
Val_in1
Sel (dst)
mux2
Value coming from either reg1,2,3 or 4
Val_in2
Val_in3
Val_in4
Val_out
entity mux2 is port (
sel:in std_logic_vector (1 downto 0);
en:in std_logic;
val_in1,val_in2,val_in3,val_in4: in std_logic_vector (3 downto 0);
val_out: out std_logic_vector (3 downto 0) :="0000");
end mux2;
architecture m2 of mux2 is
begin
val_out<=val_in1 when (sel="00" and en='1’)
else val_in2 when (sel="01" and en='1')
else val_in3 when (sel="10" and en='1’)
else val_in4 when (sel="11" and en='1’)
else "0000";
end m2;
en
Dst_reg_en: Enable to send value from destination register

## Slide 39
Demultiplexer A
MUXA
MUXB
Start

## Slide 40
Val_in
sel
dmuxa
Val_out
Display_out
entity dmuxa is port(
val_in:in std_logic_vector (3 downto 0);
sel:in std_logic;
val_out:out std_logic_vector(3 downto 0) :="0000";
display_out:out std_logic_vector(3 downto 0) :="0000");
end dmuxa;
architecture da of dmuxa is
begin
val_out<=val_in when sel=‘0’;
display_out<=val_in when sel='1’;
end da;
ssd : Enable for display content of dsp register on 7seg
Display
Value coming from dst reg

## Slide 41
7 Segment Display
MUXA
MUXB
Start

## Slide 42
6
4
1
0
2
5
3
6
4
1
0
2
5
3
entity display is port (
val_in:in std_logic_vector (3 downto 0);
disp1,disp2:out std_logic_vector(0 to 6):="1110111");
end display;
architecture d of display is
begin
disp1<="1110111" when val_in="0000" or val_in="1010" else
"0100100" when val_in="0001" or val_in="1011" else
"1011101" when val_in="0010" or val_in="1100" else
"1101101" when val_in="0011" or val_in="1101" else
"0101110" when val_in="0100" or val_in="1110" else
"1101011" when val_in="0101" or val_in="1111" else
"1111011" when val_in="0110" else
"0100101" when val_in="0111" else
"1111111" when val_in="1000" else
"1101111" when val_in="1001";
isp2<="1110111" when val_in="0000" or val_in="0001" or val_in="0010" or
val_in="0011" or val_in="0100" or val_in="0101" or
val_in="0110" or val_in="0111" or val_in="1000" or
val_in="1001" else
"0100100" when val_in="1010" or val_in="1011" or val_in="1100" or
val_in="1101" or val_in="1110" or val_in="1111" ;
End d;
Display
disp1
disp2

## Slide 43
1 | 1 | 0 | 0 | H | L | DST | DST
7 6 5 4 3 2 1 0
H=1 => display value in reg2 on 7seg display

## Slide 44
6
4
1
0
2
5
3
6
4
1
0
2
5
3
Disp1
Disp2

## Slide 45
Multiplexer B
MUXA
MUXB
Start

## Slide 46
Val_in
en
muxb
Val_out
entity muxb is port (
val_in:in std_logic_vector (3 downto 0);
ci_out:in std_logic;
en:in std_logic;
val_out:out std_logic_vector (3 downto 0) :="0000");
end muxb;
architecture mb of muxb is
signal tmp:std_logic_vector(3 downto 0);
begin
tmp<="000" & ci_out;
val_out<=tmp when en='1' else val_in;
end mb;
Ci_out
Ci_out_en : Enable ci_out input to muxb

## Slide 47
ALU
MUXA
MUXB
Start

## Slide 48
A
B
OP
R
Cout
Overflow
MUXA
MUXB
ADDSUB
TMP(0)<='0';
TMP(1)<=B(1) when op='0' else not B(1);
TMP(2)<=B(2) when op='0' else not B(2);
TMP(3)<=B(3) when op='0' else not B(3);
FA0:full_adder port map(A(0),B(0),OP, R(0),C1);
FA1:full_adder port map(A(1),TMP(1),C1, R(1),C2);
FA2:full_adder port map(A(2),TMP(2),C2, R(2),C3);
FA3:full_adder port map(A(3),TMP(3),C3, R(3),C4);
OVERFLOW <= C3 XOR C4 ;
Cout <= C4;
R<=res(3) & res(2) & res(1) & res (0);
entity alu is
port( OP: in std_logic;
A,B : in std_logic_vector(3 downto 0);
R : out std_logic_vector(3 downto 0):="0000";
Cout, OVERFLOW : out std_logic);
end alu;
signal C1, C2, C3, C4: std_logic:='0';
signal TMP: std_logic_vector(3 downto 0);
signal res:std_logic_vector(3 downto 0);

## Slide 49
Temporary Register
MUXA
MUXB
Start

## Slide 50
D
Sync_Reset
Q
CLK
Temp_reg
Src_reg_en
if(rising_edge(Clk)) then
if(sync_reset='1') then
Q <= (others => '0');
elsif(src_reg_en = '1' or dst_reg_en='1’)then
Q <= D;
end if;
end if;
dst_reg_en
Src_reg_en: Enable to send value from source register along carry to ALU
dst_reg_en: Enable to send value from destination register

## Slide 51
Multiplexer C
MUXA
MUXB
Start

## Slide 52
SW_in
Alu_out
muxc
Val_out
entity muxc is port (
sw_in:in std_logic_vector (3 downto 0);
Tmp_in:in std_logic;
Alu_out,din:in std_logic;
val_out:out std_logic_vector (3 downto 0):="0000" );
end muxc;
architecture mc of muxc is
Begin
val_out<=sw_in when din='1' else tmp_in when alu_out=‘1’;
end mc;
Tmp_in
7 6 5 4 3 2 1 0
Instruction or data
din
din: Enable for inputs bits loaded into register pointed by dst
Alu_out: Enable for output of alu to go to dest reg

## Slide 53
Demultiplexer B
MUXA
MUXB
Start

## Slide 54
Val_in
Sel (dst)
dmuxb
Regd_1
entity dmuxb is port(
val_in:in std_logic_vector (3 downto 0);
alu_out,din:in std_logic;
sel:in std_logic_vector (1 downto 0);
regd_1,regd_2,regd_3,regd_4:out std_logic_vector(3 downto 0);
end dmuxb;
architecture db of dmuxb is
begin
regd_1<=val_in when sel="00" and (alu_out='1' or din='1');
regd_2<=val_in when sel="01" and (alu_out='1' or din='1');
regd_3<=val_in when sel="10" and (alu_out='1' or din='1');
regd_4<=val_in when sel="11" and (alu_out='1' or din='1’);
end db;
Regd_2
Regd_3
Regd_4
reset
reg
en1
q1
en2
en3
en4
q2
q3
q4
d1
d2
d3
d4
Alu_out
din
Alu_out: Enable for output of alu to go to dest reg
din: Enable for inputs bits loaded into register pointed by dst

## Slide 55
Add src reg along with carry with dest reg and put result in dest reg
Op | Op | CC | CC | SRC | SRC | DST | DST
7 6 5 4 3 2 1 0
Reg2
Reg1
Reg1

## Slide 56
Carry=1

## Slide 57
THANK YOU!
QUESTIONS?